## Slide 1
🚆 PASHUPATASTRA
AI-Assisted Railway Maintenance Scheduling & Disruption Recovery
Phase 1 Domain Review & Synthetic Railway Data Architecture
WORKSTREAM PRESENTATION FOR TEAM MILESTONE 1 -> PHASE 1
• Presenter / Domain Lead: Darshini (feature/domain-data) • Integration & Backend Lead: Aryan (feature/backend-api) • Smart India Hackathon 2026 | Milestone 1 Verified -> Domain Freeze Complete

## Slide 2
1. The Railway Problem & Domain Mission
Why realistic domain modeling matters for Indian Railways
THE PROBLEM WE ARE SOLVING
• Tracks are shared by high-speed express trains and freight.
• Maintenance requires track 'possessions' (total traffic block).
• Available windows are extremely tight (Night & Midday off-peak).
• Emergencies happen daily (rail fractures, OHE faults, delays).
• Manual section controllers struggle to balance safety, priority, and minimal train disruption.
DARSHINI'S MISSION (DOMAIN + DATA)
• Define the mathematical & operational truth of Indian Railways.
• Conduct thorough Domain Review (DOMAIN_REVIEW.md).
• Protect shared contracts so teammates don't break each other.
• Build deterministic synthetic data generator (generator.py).
• Provide rich, reproducible corridor fixtures (Scenarios A, B, C) for the entire pipeline.

## Slide 3
2. End-to-End System Pipeline
How Darshini's data feeds each teammate across the 6 stages
STAGE 1: DOMAIN & DATA — [Darshini]
Assets, Corridors, Synthetic Scenarios A/B/C
STAGE 2: ML RISK SCORER — [Ayush]
Priority & Risk Scoring based on Asset Defect/Criticality
STAGE 3: CP-SAT OPTIMIZER — [Tyagi]
Optimal Schedule, Committed Block Protection, Infeasibility
STAGE 4: FASTAPI BACKEND — [Aryan]
REST Endpoints: POST /optimize, /health, /disrupt
STAGE 5: OPERATIONS UI — [Archit]
Corridor Timeline Dashboard (Time x Tracks)
STAGE 6: DISRUPTION SIM — [Tirth]
Inject Disruption -> Trigger Recovery Re-solve

## Slide 4
3. Domain Review: 5 Core Decisions for Domain Freeze
Agreed railway architecture preventing downstream integration breakages
1. Track Modeling
Keep string track_id ('UP-1', 'DOWN-1') for zero solver breaking changes. Attach rich corridor metadata in data layer.
2. Work Types
Standardized 6 Indian Railways categories: Track Renewal, Tamping, OHE, Signalling, Inspection, Emergency Repair.
3. Machinery Constraints
Model heavy track machines via mutual_exclusion_group (e.g. BCM_01, CSM_01). Prevents solver RCPSP bloat & timeouts.
4. Train Timetable
Train traffic represented as 24-hour discrete Possession Windows (Night, Midday, Evening). Blocks must fit inside windows.
5. Disruption Scenarios
Defined 4 deterministic disruptions (Track Unavailable, Emergency Injection, Possession Curtailment, Machine Breakdown).

## Slide 5
4. Maintenance Categories & Operational Windows
Operational characteristics for Tyagi (Optimizer) & Ayush (Scorer)
6 MAINTENANCE CATEGORIES (WorkType)
• 1. TRACK_RENEWAL (180-240m): Heavy BCM machine, CTR/TSR
• 2. BALLAST_TAMPING (90-150m): Tie-tamper CSM, packing
• 3. OHE_MAINTENANCE (75-120m): Tower wagon, power block
• 4. SIGNALLING_INTERLOCK (60-120m): Point machines & circuits
• 5. ROUTINE_INSPECTION (45-90m): USFD flaw detection
• 6. EMERGENCY_REPAIR (90-150m): Fracture repair (Priority 0.99)
24-HOUR POSSESSION SLOTS (1440 MIN)
• NIGHT TRAFFIC BLOCK (00:30 - 05:00 | 0030-0300 min) Primary heavy renewals, tamping, and track machines.
• MIDDAY MAINTENANCE SLOT (11:30 - 14:30 | 0690-0870 min) Inspections, OHE isolations, point adjustments.
• EVENING OFF-PEAK SLOT (21:00 - 23:30 | 1260-1410 min) Signalling, track circuits, minor urgent repairs.
• HEADWAY SAFETY BUFFER: 15 minutes between consecutive blocks on the same track.

## Slide 6
5. Synthetic Scenario Datasets (Generator Output)
Deterministic, seed-driven corridor benchmarks exported as JSON fixtures
SCENARIO A: BASELINE MAINLINE (corridor_a_blocks.json)
seed=42 | 2 Tracks (UP-1, DOWN-1) | 12 Block Candidates
• 100% clean feasible schedule. • Precedence chain: BLK-003 (Renewal) -> BLK-004 (Tamping). • 2 shared machine groups (BCM_MACHINE_01, CSM_TAMPER_01). • Perfect starting fixture for Tyagi's CP-SAT solver and Archit's UI.
SCENARIO B: HIGH-DENSITY QUADRUPLE (corridor_b_dense.json)
seed=101 | 4 Tracks (UP-1, UP-2, DOWN-1, DOWN-2) | 24 Block Candidates
• Simulates 4-track trunk corridor (New Delhi - Kanpur). • 4 competing machine groups under tight possession windows. • Tests CP-SAT solver trade-offs, capacity saturation, and priority ranking.
SCENARIO C: DISRUPTION & RE-OPTIMIZATION (corridor_c_disrupted.json)
seed=999 | 2 Tracks (UP-1, DOWN-1) | 14 Block Candidates
• Pre-configured with 2 COMMITTED blocks on DOWN-1 (01:00-03:15). • Ready for Tirth's simulation to inject TRACK_UNAVAILABLE on UP-1 (02:00-05:00). • Proves solver re-optimizes remaining blocks while protecting committed work.

## Slide 7
6. Deliverables, Test Results & Teammate Handover
All Phase 1 goals verified and ready for team freeze
10/10 AUTOMATED TESTS PASSED (0.049s)
✓ test_seed_reproducibility [PASSED]
✓ test_track_assignment_validity [PASSED]
✓ test_time_window_consistency [PASSED]
✓ test_dependency_integrity [PASSED]
✓ test_work_types_are_valid_enums [PASSED]
✓ test_score_boundaries [0.0, 1.0] [PASSED]
✓ test_scenario_b_dense_properties [PASSED]
✓ test_scenario_c_committed_blocks [PASSED]
✓ test_json_fixtures_validity [PASSED]
✓ test_different_seeds_produce_variation [PASSED]
EXACT HANDOVER FOR TEAMMATES
• Aryan (Backend): DOMAIN_REVIEW.md is complete. Contracts in contracts/schemas.py are frozen & locked.
• Tyagi (Optimizer): Run your solver on corridor_a_blocks.json. Machine exclusions & dependencies ready.
• Ayush (ML Scorer): Asset models in models.py have criticality, condition, and defect attributes ready.
• Tirth (Simulation): Scenario C has committed blocks ready for your TRACK_UNAVAILABLE test.
• Archit (Frontend): Load corridor_a_blocks.json immediately to build the timeline UI.